## Slide 1: 物聯網框架標準
廖冠雄 助理教授
義守大學 資訊工程學系
e-mail：ghliaw@isu.edu.tw

## Slide 2: 大綱
前言
Service Framework
Architectural Framework

## Slide 3: Requirements for IoT Architecture
Interoperability
  In the way in which software interacts with physical resources
  Decouple IoT devices from the software that manages them
  Discovery, Management and Reporting, Security, Authorization
Scalability
  Large number of devices, users, interactions, connections
  Scale-less interaction

## Slide 4: Requirements for IoT Architecture
Technology Reuse and Modularity
  Software, networks, protocols, data models
  Across vendors in a vertical application segment
  Across diverse vertical application segments
Low Barrier to Innovation
  Anyone can participate and innovate

## Slide 5: IoT Service Frameworks
The goal – providing same qualities as web services to IoT
In the context of the Internet and the WWW
  Any Web Browser works with any web service, more or less
  Regardless of wire protocols used in the network
  Regardless of the data models and content types
  Across vertical application segments
  The WWW scales to planetary size
  Low barrier to Innovation

## Slide 6: IoT Service Frameworks
Internet and WWW Design Patterns
  Narrow Waist, endpoint oriented
    Innovation happens at the endpoints, enabled by common, openly available network protocols (the narrow waist)
  Layered Protocols
    Common set of IP protocols (TCP, UDP) abstract the lower communication layers
    Common Application Protocols (HTTP, REST) abstract resources

## Slide 7: IoT Service Frameworks
Internet and WWW Design Patterns
  Uniform Addressing
    URIs and Hyperlinks point to resources
    IP Addresses, DNS names are globally unique
  Stateless Interaction
    Client-Server pattern
    Hypermedia As The Engine Of Application State

## Slide 8: IoT Service Frameworks
How Does it Apply to IoT?
  Internet Protocol (IP) on Constrained Devices
  Machine to Machine (M2M) Application Protocols
  Standard Object Models and Data Models
  Hypermedia for Machine APIs

## Slide 9: IoT Architectural Frameworks
Enabling cross-domain interaction and platform unification
  system compatibility
  interoperability
  functional exchangeability
Covering the architectural needs of the various IoT Application Domains

## Slide 10: In this course, we briefly intro …
Service Frameworks
  Allseen AllJoyn
  OIC Core Framework
  OMA LWM2M
  Thread
Architectural Frameworks
  oneM2M
  ETSI M2M
  IEEE P2413

## Slide 11: Allseen AllJoyn (1)
Allseen Alliance
  Enable industry standard interoperability between products and brands with an open source framework for IoT
  Main members
    Qualcomm, Microsoft, Philips, LG, …

## Slide 12: Allseen AllJoyn (2)
What is the AllJoyn Framework?
  An open source API framework for the Internet of Everything
  A way devices and applications publish APIs over a network in a standard way
  the “things” on the network expose to other “things”
  provides application discovery and fine-grained discovery of the APIs supported by applications

## Slide 13: Allseen AllJoyn (3)
High-Level System Architecture
AllJoyn Bus is composed of two types of nodes:
AllJoyn Router (R)
Applications (App)
  App can only connect to R
  App can contain R
  R can connect to other R
The AllJoyn framework can be thought of as a
mesh of stars

## Slide 14: Ad Hoc Bus Formation: Discover
Device
Find interface org.allseen.media. audio
Implement interfaces org.allseen.media.audio org.allseen.media.video
…
Eureka!
Interface descriptions contained in About message
 Services advertise, and Clients find, About messages
 Connect to advertisers supporting desired interfaces
Actual discovery mechanism is transport-dependent:
 On Wi-Fi, PLC, Ethernet: lightweight IP multicast protocol
 On Wi-Fi Direct: would use pre-association discovery
Service App Router
Device
Client App
Router

## Slide 15: Ad Hoc Bus Formation: Session Creation
Session creation will cause AllJoyn Routers to connect and extend the bus
 Once connected, buses merge and have a single shared namespace
 Peers can discover when other peers join or leave the bus
 Peers can interact via their APIs
 Session reference counting keeps device-to-device connections alive
 Multicast events can be sent to all peers in the session
Device
Device
Client App
Service
Router App
AllJoyn Distributed Bus Router
Peer Session
Connect to
org.allseen.media. audio

## Slide 16: AllJoyn Software Framework: High-level architecture
A comprehensive software framework lets devices and applications communicate

## Slide 17: Two Versions of the AllJoyn Framework To Choose

## Slide 18: Introduction to OIC – Optimized for IoT
Common Platform
CoAP for Constrained Devices
Full Stack Interop. Test
Certification Program
RESTful Architecture

## Slide 19: OIC Key Concepts (1/2)
Open-source Implementation – Iotivity project (https://www.iotivity.org/)
Free IPR License (Code: Apache 2.0 & Spec: RAND-Z)
  License covers both code, standards and related IPR
  License applies to members and affiliates of members
Dedicated and optimized protocols for IoT (e.g. CoAP)
  Specific considerations for constrained devices
  Fully compliant towards RESTful architecture
  Built-in discovery and subscription mechanisms
Standards and Open Source to allow flexibility creating solutions
  Able to address all types of devices, form-factors, companies and markets with the widest possibility of options
  Open Source is just one implementation to solve a problem

## Slide 20: OIC Key Concepts (2/2)
Full stack definition for maximum interoperability
  Connectivity, Platform and Vertical Services defined
  License applies to members and affiliates of members
Certification and Logo program
  Guarantees all devices work together
  Consistent user awareness for interoperability

## Slide 21: Sample of Current Members
Gold
Diamond
Platinum

## Slide 22: Objectives
Core Framework Specification Scope
  Specifies the technical specification(s) comprising of the core architectural framework, messaging, interfaces and protocols based on approved use-case scenarios
  Enables the development of vertical profiles (e.g. Smart Home) on top of the core
Architect a core framework that is scalable from resource constrained devices to resource rich devices
Evaluate technical specification(s) for maximum testability and interoperability
Ensure alignment with OIC open source releases

## Slide 23: OIC Roles
OIC Client
  i) Initiate an transaction (send a request) & ii) access an OIC Server to get a service
OIC Server
  i) host OIC Resource & ii) send a response & provide service

## Slide 24: OIC Architecture
OIC adopted RESTful Architecture
Current OIC Architecture defines 2 logical roles that devices can take
  OIC Server : A logical entity that exposes hosted resources
  OIC Client : A logical entity that accesses resources on an OIC Server
OIC
Client
Model 1
OIC
Server
R

## Slide 25: Organization of an OIC Device
OIC Device concept
Physical Device e.g. light bulb
OIC Device 2
OIC Device 1
/oic/p
/oic/res
/oic/res
/oic/d
/oic/d
/oic/prs
/oic/mnt
Resource URI: /oic/p
rt: oic.wk.p
if: oic.if.r
n: homePlatform policy: bm:11
pi: at1908 mnmn: Samsung
Mandatory
Optional

## Slide 26: Device example: light device (oic.d.light)

## Slide 27: OIC Spec Features – Core Framework Spec
① Discovery: Common method for device discovery (IETF CoRE)
② Messaging: Constrained device support as default (IETF CoAP) as well as protocol translation via intermediaries
③ Common Resource Model: Real world entities defined as data models (resources)\
④ CRUDN: Simple Request/Response mechanism with Create, Retrieve, Update, Delete and Notify commands
⑤ Device Management: Network connection settings and remote monitoring/reset/reboot functions
⑥ ID & Addressing: OIC IDs and addressing for OIC entities (Devices, Clients, Servers, Resources)
⑦ Security: Basic security for network, access control based on resources, key management etc

## Slide 28: OIC Core Framework Basic Operation

## Slide 29: Protocol Stack
30

## Slide 30: OMA LWM2M
OMA – Open Mobile Alliance
LWM2M – Light-Weight M2M
  to serve the IoT market with a focus on lightweight nature

## Slide 31: Features

## Slide 32: OMA LWM2M Architecture
M2M Applications
  Application abstraction through REST API
  Resource Discovery and Linking
LWM2M Clients are Devices
  Device abstraction through CoAP
  LWM2M Clients are CoAP Servers
  Any IP network connection
LWM2M Server
  Reuses IETF technologies, such as the CoAP protocol, DTLS, Resource Directory.
  Deployable on gateways and in the cloud

## Slide 33: What is Thread?
A secure, wireless mesh networking protocol that:
Supports IPv6 addresses and simple IP bridging
Is built upon a foundation of existing standards
Is optimized for low-power / battery-backed operation
Is intended for control and automation (250kbps)
Can support networks of 250 nodes or greater
Supports low latency (less than 100 milliseconds)
Offers simplified security and commissioning
Runs on existing 802.15.4 wireless SoCs
http://www.threadgroup.org/

## Slide 34: Connected Home – Networking Requirements
Direct addressability of devices – within the HAN and from smart phones or tablets
•
Simplified forming and joining of network, limit special devices or customer knowledge of concepts like coordinator vs. router vs. end device
Scalable to 200-300 devices in a home – with sufficient routers to provide coverage but remainder can be end devices
Allow the use of multiple gateways
Latency less than 100 milliseconds for typical interactions (user interaction concern)
•
•
Seamless connectivity to user interaction on device of choice in the home (dedicated display, smart phone, tablet, etc.)
Battery operated devices with years of expected life – door locks, security sensors etc.

## Slide 35: Target Devices
•
Normally Powered
Gateway
Lighting
Appliances
Smart Meter
Garage door opener
HVAC equipment
Smart Plugs
Fans
•
Powered or Battery
Thermostat
Light switches
Smoke detectors
In home display
Shades or blinds
Door bell
Glass break sensors
Robots/cleaners
Normally Battery
Door sensors
Window sensors
Motion sensors
Door locks
Radiator valves
Body sensors

## Slide 36: System Messaging Model
Cloud connectivity for control when not at home
When within the home, phone or tablet must go direct to gateway to reduce latency
Has to be seamless to consumer using device
Border Router forwards data to cloud
Also provides WiFi connectivity to phone or tablet in the home
Expect device to device communication within HAN for operations in the home
Thread
HAN

## Slide 37: Key Features Overview
IP-based:
Simplified bridging to other IP networks
Flexible Network:
Simplified device types
Robust:
No single point of failure
Secure:
Simple security and commissioning
Low Power Operation:
Support for sleeping devices
Physical Radio (PHY)
IEEE 802.15.4 MAC
(including MAC security)
IPv6
Distance Vector Routing
UDP + DTLS
Application Layer
IEEE 802.15.4 (2006)
RFC 4944, RFC 4862, RFC
6282, RFC 6775
RFC 1058, RFC 2080
RFC 768, RFC 6347, RFC
4279, RFC 4492, RFC 3315,
RFC 5007
Thread
Standard
6LowPAN

## Slide 38: oneM2M – The Common Service Layer

## Slide 39: oneM2M – Common Service Functions

## Slide 40: oneM2M – Technical Reports

## Slide 41: oneM2M – Technical Specifications

## Slide 42: oneM2M – Use Cases & Requirements

## Slide 43: oneM2M - Architecture

## Slide 44: oneM2M - Architecture

## Slide 45: ETSI M2M - High Level Architecture

## Slide 46: ETSI M2M - Architecture

## Slide 47: ETSI M2M - Example

## Slide 48: ETSI M2M – High Level Deployment

## Slide 49: IEEE P2413
Focus to integrate market needs with the developing IoT technology landscape
Define an Architectural Framework for the IoT
  descriptions of various IoT domains
  definitions of IoT domain abstractions
  identification of commonalities between different IoT domains

## Slide 50: IEEE P2413
The Architectural Framework for IoT provides
  reference model
    defines relationships among various IoT domains
  reference architecture
    builds upon the reference model
    defines basic architectural building blocks and their ability to be integrated into multi-tiered systems
    addresses how to document and mitigate architecture divergence.

## Slide 51: IEEE P2413 Definitions
The Group accepted the definition of the “Thing”:
Security
Function/Method
Information Exchange
Properties
The “Thing”
Apps & Services
Notes:
Things, Apps, and Services can be integrated into what would be abstracted as a “Thing”
Information exchange could be “horizontal” (subscribe/ publish as an example) or vertical, or both
Properties could be real or virtual

## Slide 52: IEEE P2413 Levels of abstractions
Universal Thing Description
Who am I Who makes me What can I do
Where do you go to get more info Who is asking
What language do I talk

## Slide 53: IEEE P2413 Structure

## Slide 54: IEEE P2413 Potential Profiles